(New or existing construction)  09/09/21                                                                                       															CONSTRUCTION EXHIBIT

GENERAL SPECIFICATIONS

ABC WHOLESALE

These specifications are all inclusive. Any deviation of product schedules or plans must have prior approval of ABC Board, before purchase or installation, in writing and will become part of the lease file. This building must meet all requirements of the “American with Disabilities Act” and must comply with all Local and State Building Codes. All work will be completed before acceptance.

Owner will furnish any required licenses, permits or architectural drawings that may be required. All drawings must be submitted to ABC Board for approval before work begins. Before any changes are made the ABC Board must be notified for approval.

GENERAL SPECIFICATIONS

NOTE: NO EQUALS WILL BE ACCEPTED. SOME ITEMS WILL HAVE ALTERNATES LISTED. ONLY THOSE ALTERNATES WILL BE ACCEPTED. WHERE ALTERNATES ARE NOT LISTED, ONLY THAT ITEM WILL BE ACCEPTED.

NOTE: Item #1 is for new construction only!

- Construct a Pre Engineered Metal Building (PEMB), Color to be selected by ABC Board. Building will have sloped roof to the rear of the building. Roof to be a Standing Seam type. Building will be insulated with vinyl insulation for PEMB. Warehouse area will be constructed of metal sheathing on the outside and on the inside for security purposes.

- Construct six foot (6’) sidewalk at along the entrance of building and a five foot (5’) sidewalk down the side of the building designated for parking. Construct handicap ramp as required as per ADA Standards. Alternate: If parking lot is Concrete, Sidewalks may be incorporated as part of the concrete paving and constructed flush. Concrete should slope away from building for drainage purposes. Slope at sidewalk and parking should meet ADA Standards. Steel Bollards should be installed along entrance and concrete wheel stops should be installed at all designated parking.

- The parking lot and truck delivery area must be constructed of concrete paving. Truck delivery area should be sized to allow truck to access warehouse.

- All designated parking should be striped on nine foot (9’) minimum widths and include the required number of handicap spaces and signage. Construct handicap accessibility as per ADA Standards. Parking lot will be clean before ABC will take occupancy.

- Install one (1) commercial bronzed aluminum-glass door and window glass (energy star rated see item 23 for ratings) at the entrance. A dry covering will be required over entrance doors with adequate lighting.

- The walls in the office and sales area are to be sheetrock floated for paint and must be smooth and free of any offsets or protrusions and debris.

- The check-out counter will be provided and installed by the Landlord. The counter must be boxed in with one adjustable shelf and a 16” D x 20” W x 4”D  pencil drawer for each cash register the drawer has to be at least 3” off the back wall.  The tops of the counters will be covered with Black Granite with 2” overhang.   The counter front will be stacked Stone real or faux Stone (see Check Out Counter Specs) this will be a decision made by ABC.   The shape and length of the counter will be determined by ABC Board (depending on number of cash registers to be used).

- Construct a 24” W X 36” L X 42” H Wall mounted table in warehouse with electrical service as well as phone and data line connections. To be located on the wall at end of staging tables.  The tops of the table will be coved with Formica Matte finish color #837-58 the sides #3202-58. Table to be provided and installed by the Landlord.

- Construct two (2) Staging/Work Tables 36”W x 120”L x 35 3/4” H made of heavy iron. ( See Attached) Tables to be provided and installed by the Landlord.

- Install a suspended ceiling (Armstrong Fissured #756A 2’x2’ Panels) nine feet (9’) above the floor in the entire office and sales area with a minimum of six inches (6”) of insulation. The ceiling grid will be black in sales area and white in office area. Alternate: USG Interiors #359.  Note: Restroom ceiling will be 8’ AFF.

- Install HVAC to adequately heat or cool the entire building, (units will be energy star rated with a SEER rating of 15 or better). Return air vents must be ceiling mounted. Air filters for the HVAC are to be rated MERV 8 and are changed quarterly by the Landlord. Note: Install programmable thermostats for office area. Warehouse area should be adequately heated and cooled.

- Provide a ¾” x 4’ x 12’ fire rated plywood panel (painted with fire rated paint) mounted horizontal adjacent to the electrical panel or in mechanical closet for phone, alarm system, and computer server installation. This board will be mounted 60” above finished floor. Provide 2” pipe through wall for phone line adjacent to this panel. Pipe must be a minimum of 10’ above exterior grade. In areas where phone line comes into building from underground, a conduit must be provided (with pull string) so no phone wire is exposed on the exterior. Phone service must be ordered to building by Landlord as soon as there is power to the board. Plywood panel must have a ground wire, six (6) separate quadraplex each one isolated outlets: two on left bottom corner, two in the bottom middle and two (2) separate on right bottom corner of plywood. Install standard outlets in office with one plug on each wall.  Install standard outlets in warehouse every 12 to 15 feet. In the Warehouse mount these plugs minimum of 36” above finish floor.

- Install a hollow steel commercial security door with NRP (non removable pin) hinges, a thumb deadbolt and ADA lever door handle at locations per drawings. This should be all doors except office entrance glass door. These doors will also have lock guard on the exterior. This is preventing the doors from being pried open. This door will be thirty-six inches (36”) wide.  Install a steel security bar on the inside of the door. Model Exit Security #SB010036A (Vendor – Tri State Door Company, P.O. Box 177, Hartford, AL 36344, Phone (334) 588 3462); or direct form VENDOR: Exit Security, Inc., 1-800-446-6775.

- Install an electric rollup door (more detail to follow) at each loading dock for trucks. Overhead door 610 Series and Opener (See attached for more detail).

- Install commercial industrial strip curtain door kit to prevent heat and air from escaping when doors are open. (www.gasketsandstripcurtains.com/products/commercial-industrial-strip-curtain-door-kit)

- Install a loading dock capable of accommodating a 53’ foot delivery truck.  Dock height must be at least 50 inches.  The elevation will be determined by the slope depending on the grade of the land.   If a well type dock is necessary, then a sump pump and/or drain will be installed to remove storm water.

- Install a loading dock 21 inches in height to accommodate a pick-up truck. The elevation will be determined by the slope depending on the grade of the land.   If a well type dock is necessary then a sump pump and/or drain will be installed to remove storm water.

- Construct Restrooms to include tissue holder and ADA mirror above sink. Restroom door to be three feet (3’) wide. Install necessary equipment needed for the handicapped, including assist bars (side, rear, and vertical), insulation on pipes under sink, lever type door handle.

- Building and parking lot will be cleaned before ABC will take occupancy.

- If zoning or city ordinance required garbage dumpsters to be utilized, owner will furnish and install a concrete dumpster pad and fencing per specifications provided by governing authority. ABC must be consulted on location of dumpster pad.

- All landscaping, irrigation meter (when required), shrubbery, grass, trees, and pest control exterior and interior will be furnished and maintained by Lessor throughout the terms of this lease.

- A secured outside freeze proof wall faucet will be required on the front of the building.

- Any mold remediation due to leaks will be the responsibility of the landlord.

- Furnish and install mailbox and post if necessary, as required by local postal service.

- The warehouse doors will have two (2) bollards filled with concrete, for the trucks, to prevent damage to the building and awnings.

- All door locks are to be re-keyed in presence of ABC store manager and four (4) keys given to the manager on liquor delivery date or day of acceptance.

- A “SELECT ABC SPIRITS” sign must be furnished, installed, and maintained by the landlord during the term of the lease. The size of the signs will be to local code; however, the design of the sign must be adapted. These signs will be controlled with dusk to dawn photo cell direct wired to panel. (Note: NO TIMERS) Final design must be approved by ABC Real Estate. Sign must be up and operational one week before acceptance of the store. The sign will be maintained during the term of the lease by the Landlord. Note: In the event that ABC vacates the premises the Landlord shall be responsible for removal of the signage within 30 days.

- Building should have the correct amount of fire extinguishers installed per state fire codes.

- All windows will be energy star rated U-Factor less than or equal to 0.60 and SHGC less than or equal to 0.27 and be certified by NFRC.

- In Hurricane prone areas, hurricane shutters will be required and maintained by the Landlord. It will be the landlord’s responsibility to insure they are in place during a severe weather event.

ELECTRICAL

NOTE: NO EQUALS WILL BE ACCEPTED. SOME ITEMS WILL HAVE ALTERNATES LISTED. ONLY THOSE ALTERNATES WILL BE ACCEPTED. WHERE ALTENATES ARE NOT LISTED, ONLY THAT ITEM WILL BE ACCEPTED

Due to new regulations from the Governor’s office, all leased state property must comply with the new energy savings rules. All electrical, gas, lighting, HVAC, toilets, and signs must meet these new rules and it is the Landlord’s responsibility to comply and will be held responsible for the maintenance of said throughout the term of the lease.

- Install and maintain interior lighting it will be 2’ x 4’ LED Lithonia 2GTL-4-48EZI LP840 throughout building. Pattern the fixtures with six foot (6’) width between fixtures and four foot (4’) between lengthwise.  Install one (1) fixture in each restroom.  One fixture in the sales area and 3 in the warehouse will have four lamps unswitched for night light.  Provide wiring as needed for sign, plumbing, HVAC, interior, and exterior per 2014 NEC code. It is the Landlord’s responsibility to change bulbs and maintain lighting during the terms of the lease.

- Install a 3/4” pipe connecting the checkout counters for phone line installation (with pull strings). This is to be coordinated with ABC Technical Personnel. The cash registers need 3 conduits each with pull strings penetrating through the ceiling.

- Install LED combo units Exit/Emergency light above all exit doors. Install all required LED emergency lighting as per local codes in sales and warehouse area.

- Install exhaust fan in restrooms switched separately from light. Vent exhaust through exterior wall (by mechanical contractor).

- Install and maintain LED Wall Packs 150 watt on building to adequately provide lighting on all four sides of building and under canopies. (Photo Cell Controlled) NO TIMERS

- Install one (1) standard quadplex plug in each checkout counter locations. Coordinate with ABC Technicians for details.

- The computer cash register has special wiring requirements. Contractor to coordinate with ABC Technicians for details.

- Provide a ¾” x 4’ x 12’ fire rated plywood panel (painted with fire rated paint) mounted horizontal adjacent to the electrical panel or in mechanical closet for phone, alarm system, and computer server installation. This board will be mounted 60” above finished floor. Provide 2” pipe through wall for phone line adjacent to this panel. Pipe must be a minimum of 10’ above exterior grade. In areas where phone line comes into building from underground, a conduit must be provided (with pull string) so no phone wire is exposed on the exterior. Phone service must be ordered to building by Landlord as soon as there is power to the board. Plywood panel must have a ground wire, six (6) separate quadraplex each one isolated outlets: two on left bottom corner, two in the bottom middle and two (2) separate on right bottom corner of plywood. Install standard outlets in office with one plug on each wall.  Install standard outlets in warehouse every 12 to 15 feet. In the Warehouse mount these plugs minimum of 36” above finish floor.

- Install one (1) junction box above ceiling for main sign and wiring to sub panel.

FLOOR COVERING

NOTE: NO EQUALS WILL BE ACCEPTED. SOME ITEMS WILL HAVE ALTERNATES LISTED. ONLY THOSE ALTERNATES WILL BE ACCEPTED. WHERE ALTENATES ARE NOT LISTED, ONLY THAT ITEM WILL BE ACCEPTED

- Install Porcelain Tile flooring in office areas, lobby, and restrooms. Color and product will be selected by ABC Real Estate.

- Install Cove Base color is Roppe Light Brown 147.

- If warehouse floor does not have any major flaws, use two (2) coats of concrete seal (clear). Or If the floor has flaws, seal the warehouse floor with two coats of Lowe’s Quikrete multi-surface concrete Gray 51020 and seal with two coats of  clear sealer .  Install cove base after floor dries.

PAINT

NOTE: NO EQUALS WILL BE ACCEPTED. SOME ITEMS WILL HAVE ALTERNATES LISTED. ONLY THOSE ALTERNATES WILL BE ACCEPTED. WHERE ALTENATES ARE NOT LISTED, ONLY THAT ITEM WILL BE ACCEPTED

- Exterior Doors Steel doors to be painted to match trim on the building. (Color to be determined by ABC Real Estate)

- Interior walls are to be primed and then painted with two (2) coats Sherwin Williams #7642 Pavestone Eggshell enamel. Lobby and offices will be painted from floor to ceiling. Trim color for doors will be Sherwin Williams #1028 Kohl Gloss Enamel Bronze Satin and all wood will be 2 coats of Min-Wax stain (English Chestnut) with a finish coat of Polyurethane to seal. If possible leave some of the wall and trim paint for touch-ups.

- Warehouse Painted walls and bathrooms areas will be Sherwin Williams Pro Mar 200 Egg Shell Extra White.

PLUMBING

NOTE: NO EQUALS WILL BE ACCEPTED. SOME ITEMS WILL HAVE ALTERNATES LISTED. ONLY THOSE ALTERNATES WILL BE ACCEPTED. WHERE ALTENATES ARE NOT LISTED, ONLY THAT ITEM WILL BE ACCEPTED

- Install a Williams ten inch (10”) Terrazo service sink Model #MTB3624 and a T &S service sink faucet Model #B665 BSTA as shown on the plans. Install eight feet (8’) high white FRP back splash on all sheetrock above sink. Faucet height should be thirty-two inches (32”) AFF. NOTE: Alternates for service sink is four legged heavy duty mop sink with FRP back splash.

- Install a ten (10) gallon electric water heater energy star rated (per local plumbing code) plumbed to the restroom and the mop sink. Mount over the mop sink not the bathroom.

- Install an electric water cooler energy star rated, wall mount with a backsplash. Use ABCO P8AM Westinghouse (per ADA).

- Install a freeze-proof faucet on the front of the building. This must be a keyed faucet to regulate use.

- Install American Standard eighteen inch (18”) elongated water closet or equal with plastic seat. (Per ADA) Closet height will be 17” – 19” inches. Alternate: Kohler. Use High efficiency toilets that use less water, the two options are two flushing option or pressure – assist technology for toilets. Toilets shall be energy star rated.

- Install 20” x 18” American Standard lavatory or equal. Height of lavatory will be thirty-four inches (34”) AFF. Alternate: Kohler. Provide protective cover for piping under sink (per ADA).

- Install Kohler faucet with four inch (4”) wrist handles and 6” – 9” gooseneck or equal (per ADA)

- Install handicap bathroom signs per ADA and local code. Note: ADA height requirements.

STORE FRONT SIGN

(See attached)

Furnish, install and maintain “SELECT ABC SPIRITS” signs.  The size of signs will be to local code; however, “SELECT ABC SPIRITS” design as attached must be adapted.  These signs will be controlled with dusk to dawn photo-cell direct wire to panel.  (NOTE:  NO TIMERS)

A pole sign or marquee will be required if the building visibility is limited from the street. The pole will need to be 20’- 40’ high (depending on the surrounding area.)

Final design must be approved by ABC Real Estate.  Sign must be up and operational one week before acceptance of store.

NOTE:

In the event that ABC vacates the premises the Landlord is required to have All ABC SIGNAGE removed within 30 days of termination.